## Slide 1: Zephyrus Hand Motion-Controlled Remote Car
Embedded Systems
Hugo Carvalho – A85156
José Mendes – A85951
Analysis

## Slide 2: Agenda
Problem Statement
Market Study
Requirements
Constraints
System Overview
Hardware Architecture
Software Architecture
Reinforcement Learning
Events
Uses Cases
Sequential Diagrams
State Diagrams

## Slide 3: Problem Statement
Motion-tracking and gesture-controlled robots have been gaining traction in entertainment and medical applications.
In an R&D-like approach, the project will consist of a gesture-controlled car with a wristband as a remote controller.
The user will be able to accelerate and steer the vehicle using natural wrist and finger movements.

## Slide 4: Problem Statement

## Slide 5: Market Study
Ultigesture’s arm gesture-controlled RC car
Cost: 89$
Pros:
Practical setup;
Appealing design;
The use of Bluetooth allows the car to be controlled both by arm gestures and smartphone;
Cons:
Unpractical and uncomfortable to command.
Glove-controlled RC Quadcopter Drone
Cost: 36$
Pros:
Practical and comfortable to command;
Impactful first impression;
Cheap;
Cons:
Cheap-feeling;
Can only be worn in the right hand.

## Slide 6: Added Value
Zephyrus aims for:
Good usability;
Competitive pricing;
An easy setup;
Comfortable use and control.

## Slide 7: Requirements
  Functional Requirements:
Sense the user inputs and generate the band outputs;
Take the wristband inputs and generate the desired motor outputs;
Use wireless communication between the local and remote systems;
Control the establishment and closure of the connection from the remote system.
  Non-Functional Requirements:
Have low power consumption;
Have low latency in the connection between local and remote;
Have a comfortable and practical wristband/glove.

## Slide 8: Constraints
  Technical Constraints:
Use the Nucleo-STM32F767ZI as the development board;
Use at least three different types of sensors;
Use FreeRTOS as the RTOS;
Use a controller based on Reinforcement Learning following the Actor-Critic method;
Use Keil MDK-ARM as the development environment;
Use Object-Oriented Programming Languages;
  Non-Technical Constraints:
Project deadline at the end of the semester;
Pair workflow;
Limited budget;

## Slide 9: System Overview

## Slide 10: System Overview

## Slide 11: System Overview

## Slide 12: Hardware Architecture

## Slide 13: Software Architecture
Local System
Remote System

## Slide 14: Reinforcement Learning
System Overview

## Slide 15: Reinforcement Learning
Zephyrus Edge Machine Learning Framework

## Slide 16: System Events
Local System
Remote System

## Slide 17: Local System Use Cases

## Slide 18: Remote System Use Cases

## Slide 19: Local System Sequence Diagrams

## Slide 20: Local System Sequence Diagrams

## Slide 21: Remote System Sequence Diagram
1
1

## Slide 22: Local System State Diagram
2

## Slide 23: Local System State Diagram
2

## Slide 24: Remote System State Diagram

## Slide 25: Estimated Budget

## Slide 26: Gant Diagram